TITLE:                          PROPER USE OF A LABORATORY CENTRIFUGE

SAFETY EQUIPMENT:	Lab coat, safety glasses, gloves

PROCEDURE:	Using a Laboratory Centrifuge

# LOAD SAMPLES

# Select the appropriate centrifuge based on the volume of the sample(s) and the desired speed and temperature.

# Ensure that the centrifuge is located on a rigid, flat, level surface.

# Remove or lift cover from centrifuge.  Insert sample(s) into the rotor making sure to place two samples opposite of each other to maintain balance.

- If an odd number of samples need to be spun, make a counterbalance by filling an empty test tube or microcentrifuge tube with an equal volume of water.

- Securely screw on or close the lid of the centrifuge

# CENTRIFUGE OPERATION

# Set the desired speed, time, and temperature (if applicable) on the centrifuge.

# Press the “Start” button and wait for the instrument to ramp up to the desired speed.

# Note: It is normal to see a small vibration in the instrument as the speed increases, but any large vibration in the instrument or irregular noise may indicate that something has gone wrong with the run.  Press the “Stop” button and make sure that the tubes are balanced properly.

# When the run has completed and the rotor has come to a complete stop, unscrew the rotor lid and carefully remove the samples to prevent resuspension of the sediments.